## Slide 1: SDR Dongle Our “Eye” to the Wireless World
Mario Filippi, N2HUN, WQWL238
2016 Trenton Computer Festival
m51f08@yahoo.com

## Slide 2: Wireless Communication is Not Novel
Speech
Handwriting
Sign language
Whistlers of Gomera Island (Canary Is)
Body language
Semaphore
Smoke signals
Signal drums
Mail
Pony Express
Homing pigeon
Road signs
Pheromones – animal and insect world
Bugle at reveille

## Slide 3: RF Spectrum
Long wave 150 – 530 KHz
Medium wave 530 – 1710 KHz
Short wave (HF) 1.710 – 30 MHz
VHF 30 – 300 MHz
UHF 300 – 3000 MHz
SHF 3000 – 30 GHz

## Slide 4: Basic Wireless Device Anatomy
Transmitter
Receiver
Voice (AM, FM), Data (ASK, FSK, OOSK)

## Slide 5: Wireless Devices - Home
54 -216, 470-698 MHz
540-1710 KHz
88-108 MHz
1921-1928 MHz Tx/Rx
315 MHz Tx
315.6 MHz Tx
390.46 MHz Tx
315 MHz Rx
390.46 MHz Rx
315.6 MHz Rx
Satellite
C band: 3.7-4.2GHz
Ku band: 11.7-12.2 GHz
Subscription sat band: 12.2-12.7 GHz
IPod

## Slide 6: Wireless Home Devices – Home (Cont’d)
915.5 MHz Tx
2.432 GHz
915.5 MHz Rx
314.449 MHz Tx
900 MHz ISM (1W) band/2.4 GHz
2.480 GHz
824 – 849 MHz (2G)
2.412-2.462 GHz
2.402-2.480 GHz
2.412-2.462 GHz
2.4, 5 GHz

## Slide 7: Wireless Devices – Vehicles
Ford Fiesta
Console: AM/FM/Satellite
AM/FM/Satellite Antenna
Sirius/XM Satellite Radio
2.332-2.348 GHz
390.46 MHz Tx
“Smart” Visor for Garage Door/Indoor Light
Smart Visor Dipole Antenna
Global Positioning System
1.227/1.575 GHz
Wireless entry, remote starter
315 MHz Tx
434 MHz Tx
FM Wireless Xmitter, 88-108 MHz

## Slide 8: Wireless Devices – Vehicles (cont’d)
LoJack - 173.075 MHz
Rear view backup camera – 2.4 GHz
TPMS 315, 434 MHz (ASK,FSK)
Wireless Sensing Devices: 900 MHz, 2.4 GHz band

## Slide 9: Wireless Devices – Hobbies
Other examples:
Drones – 2.4, 5.8 GHz
R/C cars , boats– 27, 49 MHz, 2.4, 5.8 GHz
CB: 26.965 – 27.405 MHz
2m ham: 144-148MHz
70 cm ham 440 – 450 MHz
FM Sweep Generator 5-240 MHz
RF Signal Generator: 100 KHz – 54 MHz
FRS/GMRS: 462 & 467MHz
1.8 – 2MHz, 3.5-4 MHz, 7-7.3 MHz, 14-14.35MHz, 21-21.450 MHz, 28-29.7MHz
169.505MHz
Micro-drone: courtesy of G. Vaccarino

## Slide 10: Wireless Devices – On the Job
FM wireless microphone
88-108 MHz Tx
Commercial VHF handheld 144-174 MHz or 450-470 MHz
Wireless printer
2.412-2.462 GHz
Old printers used 27 MHz band. Some now use 5.8 GHz.
3G Phone
Wireless keyboard
2.403-2.480 GHz
Wireless mouse
2.405-2.474 GHz
Old mice used 27 MHz band.

## Slide 11: What Frequency is My Wireless Device Operating On?
Look in owner’s manual or packaging
Get FCC ID # from device
Go to www.fcc.gov and do an FCC ID search
Frequency counter (moderate $, range up to 3 GHz)
Spectrum analyzer (high $ wide spectrum range)
RTL-SDR Dongle (low $, limited to 25 – 1700 MHz)
Note: Put on your Bifocals!
MFJ-866 Frequency Ctr

## Slide 12: SDR Dongle
Small broad band receiver
Originally designed to receive TV and radio broadcasts in Europe, Africa, Middle East
Plugs into USB port of computer (some Android apps available)
Needs driver + software + 5V + antenna to operate
Not a Plug ‘n Play operation
Covers frequency range 24 – 1700 MHz (Other chipsets, e.g. Elonics tuner 64 – 2300 MHz)
Low cost – well within a hobbyist’s budget
Available on-line (Nooelec, Amazon, EBay)
Modes: AM, FM, SSB, CW, some have DRM
Up to 2 MHz spectrum display
Waterfall image
Uses Zadig driver
Can use SDR#, HDSDR or other software packages such as Touchstone Pro or RTLPanorama
Useful for looking at waveforms of wireless devices, troubleshooting radio equipment, aligning/restoring radios, looking for bugs, tuning/turning antennas, checking preamp performance

## Slide 13: Setting Up a Dongle to View Waveforms
2 MHz scan of FM broadcast band using SDR#
USB pigtail
SDR “dongle”
Antenna coax
Antenna

## Slide 14: Wireless Device Waveforms - Home
Doorbell
On/Off Switch
AM/FM Radio
AM Band scan 530 – 1710 KHz
Data burst when switching On/Off
Data burst when button is pressed

## Slide 15: Wireless Device Waveforms – Home (cont’d)
AM/FM Radio
OTA TV
Garage door remote
Touchstone Pro Software
HDSDR Software
SDR# Software
Three different TV channels
Data bursts when button is pressed to open/shut door
FM Band scan 88 – 108 MHz

## Slide 16: Wireless Device Waveforms – Home (cont’d)
Sony Wireless Headset
Wireless audio signal from program on TV set
Wireless Wx Display
Remote sensor
FCC ID
Courtesy of www.fcc.gov
Remote sensor data burst

## Slide 17: Wireless Device Waveforms - Vehicles
Lock
Unlock
LoJack
Data burst
Possibly TV Channel 7 (174-180 MHz)

## Slide 18: Wireless Device Waveforms - Hobbies
Wireless mic
Hams talking on 2m
Amateur Radio HT
SDR# software
HDSDR Software
Pronouncing “four” into microphone
HDSDR audio spectrum analyzer s detects CTCSS (PL) tone
President CB Radio Restoration
Checking 2nd Harmonic Suppression
Checking Xmitter Accuracy – Ch 19 on 27.185
Harmonic Suppression on 54.37 MHz

## Slide 19: Wireless Device Waveforms – Hobbies (cont’d)
Vintage Equipment Restoration – Knight KG-652
Checking 63 MHz “Sweep”
Vintage Equipment Check out– Knight KG-686
Sweeping
45 MHz signal, 1000Hz external modulation
45 MHz signal, 1000Hz internal modulation
Houston we have a problem!!!!!!
0% modulation
20% modulation
No modulation – problem with circuit
Ku band dish. Downlink 11.7-12.2 GHz
LNB down converts (LO=10.750GHz)
Rx frequency =950-1450 MHz
Telstar 12 Transponder

## Slide 20: Wireless Waveform Screen Captures – Miscellaneous
Hi Def (HD) Radio - WOR, 710 KHz
RDS (Radio Data System) – WPST -FM
162.4-162.55 MHz NOAA Weather Stns.
NOAA Weather Satellite + WXtoIMG
DGPS Beacon using MultiPSK
WEFAX Station – Fldigi Software
RTTY Signal decoded via MMTTY
JLENS Radar Blimp
FLEX Pager

## Slide 21: Wireless Waveform Screen Captures – Miscellaneous (cont’d)
ADS-B on 1090 MHz
Transposed Coaxial Collinear Antenna
ADS-B Scope Software
APRS – 144.390 MHz
Wideband discone
MultiPSK decoding
10m CW Beacons
2G Cell phone - Dialing
Cell phone tower (downlink)

## Slide 22: Even More Wireless Waveform Screen Captures – (cont’d)
Decoding ACARS Using PDW
2m Ham Band During Jan. ‘16 Blizzard
Air Traffic Band During Jan. ‘16 Blizzard
Weird “Corkscrew” Signal
Railroad Comms – 160-161 MHz
433 MHz ISM Band Cornucopia
900 MHz ISM Band Cornucopia
Antenna is very important!

## Slide 23: Sources for SDR
The Spectrum Monitor Magazine www.thespectrummonitor.com
Monitoring Times back issues www.monitoringtimes.com
QST back issues www.arrl.org/qst
www.rtl-sdr.com
www.hamradioscience.com
www.rtlsdr4everyone.blogspot.com
www.greatscottgadgets.com (Hack RF One)
www.YouTube.com
www.Nooelec.com
www.nutsaboutnets.com
www.amazon.com
www.ebay.com
Nooelec Up-converter
www.thespectrummonitor.com
Covers 1MHZ – 6 GHz!

## Slide 24: Are You a Victim of RWS (Radio Wave Sickness)?
Symptoms
  Neurological: dizziness ,irritability, headaches, insomnia, memory loss, psychosis
  Digestive: nausea, abdominal pain
  Glandular: enlarged thyroid, painful testicles, painful ovaries,
  Dermatological: hair loss, rashes, redness of the skin
  Musculoskeletal: tremors, spasms, numbness,/tingling, pain in the joints and feet
  Ophthalmological: poor vision, cataracts, burning in the eyes, floaters
  Otological: tinnitus (ringing in the ears)